# Text boxes

Features:

- 1080P HD resolution,clear and fine images,32mm*32mm;

- Support 2D/3D noise reduction,digital wide dynamic;

- Advanced H.265+/H.264 video compression,Super low rate,high definition quality of image;

- Professional anti-lightning,conform to GB/T17626.5 and  IEC61000-4-5。

- Support ONVIF;access third party;

- Support various mobile monitoring(iPhone,Android);

- Provide web、CMS、center platform management software MYEYE,provide SDK development

- Support cloud technology,easy to achieve network penetration,fro in-line and alarm information pushed

IPG-80HE20PS-SL

2.0M H.265 IP Camera Module

Parameters：

| Model | IPG-80HE20PS-SL |
| --- | --- |
| System structure | Embedded RTOS,dual-core 32bit DSP(Hi3516EV100),pure hard compression ,watch dog |
| Sensor | 2.0M CMOS sensor ,color 0.1Lux@F1.2,black/white 0.01Lux@F1.2 |
| Video compression | H.265+/H.264,support dual stream,AVI;0.1M~8Mpbs variable;1~30f/s variable |
| Image output | Main stream: 1920*1080@20fps,1280*720@25fps; sub-stream: 704*576@25fps; |
| Shutter | 1/50(1/60)s to 1/10,000s |
| Lens | N/A |
| Day and night | Support IR-CUT |
| Noise reduction | Support 2D/3D |
| Wide dynamic | Support digital |
| Auto iris | N/A |
| Audio compression | G.711,support bidrectional talk,audio&video synchronization |
| Audio interface | 1ch input,level:2Vp-p,impedance:1kΩ,support sound pick-up input;1ch output,impedance:16Ω,30mw,support microphone |
| Network interface | 1*RJ45 10/100M adaptive Ethernet port;support RTSP/FTP/PPPOE/DHCP/DDNS/NTP/UPnP etc |
| Extension interface | N/A |
| Singal interface | One photo resistance interface,one IR-CUT interface ,support photo resistance signal and IR-CUT links to IR |
| PTZ | N/A |
| Motor interface | N/A |
| Alarm I/O | N/A |
| WIFI interface | N/A |
| Reset interface | N/A |
| SD Card | N/A |
| Reliability | Comprehensive lightning protection, 7 * 24 hours 65 ℃ high temperature stable and reliable testing |
| Intelligence analysis | N/A |
| Other function | Support WEB,OSD,live video transmission,motion detect and IO alarm,front-end storage/playback/download, and center reminder and image linkage,support JPEG capture；united remote client monitoring sofaware、MYEYE;perfect SDK; |
| ONVIF | Support |
| Mobile monitoring | Support multiple mobile monitoring（iOS，Android） |
| Power | DC12V/2A input, power consumption:≤3W, |
| Dimension | 32mm*32mm |
| Other | Support POE power supply, not support any custom |